## Slide 1: CG2271 Real Time Operating Systems
Lab Lecture 3
Interrupt Programming
(Reference Guide Section 3.2)

## Slide 2: Introduction
Lab Lecture 3 – Interrupt Programming

## Slide 3: Introduction
The MCXC444 uses a priority interrupt system centred around a Nested Vector Interrupt Controller (NVIC).
  All interrupts generated by devices on the MCU pass through the NVIC:

## Slide 4: Nested vectored interrupt controller
Lab Lecture 3 – Interrupt Programming

## Slide 5: Nested Vectored Interrupt Controller
The NVIC is:
  Nested:
    Meaning that higher priority interrupts can interrupt ongoing lower priority interrupts.
    Alternatively, lower priority interrupts are delayed until higher priority interrupts are completed.
  Vectored:
    When an interrupt is triggered, execution is “vectored” to a particular interrupt service routine (ISR) to handle the interrupt.
    To facilitate this, every interrupt is assigned a number – “vector”.
    Interrupt numbers 0 to 15 are reserved for the MCU core.
      System errors, non-maskable interrupt, RESET, etc.
    Interrupts 16 and above are for various hardware units.

## Slide 6: NVIC Vectors
Core Vectors (0 to 15)

## Slide 7: NVIC Vectors
Non-core Vectors (

## Slide 8: NVIC Vectors
Non-core Vectors (

## Slide 9: External interrupts
Lab Lecture 3 – Interrupt Programming

## Slide 10: External Interrupts
Like the ATMega328P on the Arduino, GPIO pins on the MCXC444 can be configured to generate interrupts
  Divided into two groups:
    Port A
    Ports C and D are combined into one group.

## Slide 11: External Interrupts
Every port (A, C, and D) has an Interrupt Status Flag Register (ISFR), e.g. PORTA_ISFR.
  If an interrupt is trigged on a pin (e.g. PTA4), bit 4 in PORTA->ISFR would be set.

## Slide 12: Configuring external interrupts
Lab Lecture 3 – Interrupt Programming

## Slide 13: Configuring External Interrupts
We will now look at an example of how to configure an external interrupt.
  We choose SW2 on the FRDM-MCXC444 board, which is connected to PTC3.
  Gives us a chance to see how to use the combined PORTC_PORTD interrupt vector.

## Slide 14: Initial Steps
Step 0: Define SWITCH_PIN:
Step 1: Disable the PORTC_PORTD interrupt.
Step 2: Turn on clocking to Port C using SIM_SCGC5:

## Slide 15: Pull-up/down Resistors
Step 3: Enable internal pull-up resistor.
  The MCXC444 has built-in pull-up or pull-down resistors.
    Pull-up resistors: weakly drives a line high until an event (e.g. closing a switch) drives it low.
    Pull-down resistor: Weakly drives a line low until an event drives it high.

## Slide 16: Pull-up/down Resistors
  SW2 on the FRDM-MCXC444 is already pulled high:
  However just for learning purposes we will activate the internal pull-up resistor on the MCXC444.

## Slide 17: Pull-up/down Resistors
The pull-up/pull-down resistors are configured using the PE and PS bits in the PORTx_PCRy pin configuration register.

## Slide 18: Pull-up/down Resistors
  PE (Pull enable):
    0 - Disable pull-up/down resistor, 1 – Enable
  PS (Pull select):
    0 – Enable pull-down resistor if PE = 1.
    1 – Enable pull-up resistor if PE = 1
We are going to enable the pull-up resistor and so PS = PE = 1.

## Slide 19: Configure Pin as GPIO and Input
Step 4: We configure PTC3 as GPIO and as an input pin (configuring as input is optional):

## Slide 20: Configure Interrupt Triggering Type
Step 5: Configure Triggering Type.
  Like the ATMega328P, the MCXC444’s interrupts can be triggered in several ways:
  Controlled using the IRQC (Interrupt Configuration) bits of PORTx_PCRy:

## Slide 21: Configure Interrupt Triggering Type

## Slide 22: Configure Interrupt Triggering Type
Since our switch is active low (i.e. pulls PTC3 low when pressed), we will trigger on the falling edge (0b1010)

## Slide 23: Setting IRQ Priority
Step 6: Set the Interrupt Priority Level.
  The NVIC stores priority levels for each interrupt in a set of 8 interrupt priority registers (IPRs) in this format.
IPR Number

## Slide 24: Setting IRQ Priority
  Each IPR stores the priority number for four interrupts.
    Each priority is represented by a 2 bit number + 6 0’s.
  The priority levels are therefore:
    00|000000 = 0 (highest)
    01|000000 = 64
    10|000000 = 128
    11|000000 = 192 (lowest)

## Slide 25: Setting IRQ Priority
We set our SW2 button as the lowest priority:
Step 7: Clear existing interrupts and re-enable.

## Slide 26: Full Setup Code

## Slide 27: Writing the ISR
Lab Lecture 3 – Interrupt Programming

## Slide 28: Writing the ISR
To write the ISR, we need to capture the PORTC_PORTD_IRQn interrupt vector.
  This vector invokes the PORTC_PORTD_IRQHandler function.
Steps in your ISR:
  Clear the pending IRQ.
  Use the ISFR register of the relevant port (in this case port C or port D) to see if the interrupt we are interested in is triggered.
  Write a “1” to the corresponding ISFR bit to reset it back to 0.
Code is shown on next page.

## Slide 29: Writing the ISR

## Slide 30: Useful Functions and Macros
Some useful functions and macros:
  Interrupt vectors for the ports:
    PORTA_IRQn, PORTC_PORTD_IRQn
  NVIC Functions:
    NVIC_DisableIRQ(vector): Disables interrupt vector
      NVIC_DisableIRQ(PORTA_IRQn);
    NVIC_EnableIRQ(vector): Enables interrupt vector
      NVIC_EnableIRQ(PORTA_IRQn);
    NVIC_SetPriority(vector, priority): Sets the priority level of the interrupt
      NVIC_SetPriority(PORTA_IRQn, 64);
    NVIC_ClearPendingIRQ(vector): Clears pending interrupt requests.
      NVIC_ClearPendingIRQ(PORTA_IRQn);

## Slide 31: Useful Functions and Macros
IRQ Handler Names:
  void PORTA_IRQHandler() {
  }; // For Port A
  void PORTC_PORTD_IRQHandler() {
  }; // for Ports C and D

## Slide 32: Conclusion
In this lecture we looked at how to configure external interrupts on Ports A, C and D.
In the next lecture we will see interrupts again as we learn how to program the Timer/PWM Modules (TPMs) on the MCXC444.